## Slide 1
Key Priorities to address
Automation handiness for quick disposition
Consistency with PDK, across teams, across dashboards
Readability in plots/Standard Lot Report
Conciseness for Etest limitations
Structure Naming for x TCs – Best practices
TEST_CONFIG_STRUCTURE_NAME_AS_TESTED
TEST_NAME_MOD|STRUCTURE_NAME
CNAI Dashboard
Etest / Super flow format
TEST_NAME[STRUCTURE_NAME_AS_TESTED]
WIJT data pull default setting
Reference Links:
Delimiter
Test Name
Row Name
Structure Name
Library Offering
Ack: Greg, Roberto, Andrew, Habib
WW19’26
How_to_TestRow_DFT_check_in_Atlantis 6.6.3.0.docx
Important Link from Etest team on DFT check:

## Slide 2
Row Name
ROS: Library_ros_iteration
Limit to 23 chars
ROS PFT: Library_rospft_iteration
LLE-neutral PFT: Library_(polarity)cl(row-identifier)_iteration
LLE-PFT: Library_(polarity)lle(row-identifier)_iteration
WID: Library_wid(row-identifier)_iteration
Matching PFT : Library_ m(polarity)cl(row-identifier) _iteration
ISO: Library_failmode_iteration
IL Row: Library_StandardRowFormat_(il)iteration
Bit PFT : Library_bitpft(row-identifier) _iteration

## Slide 3
Structure name in Atlantis reflects on STRUCTURE_NAME_AS_TESTED on tester concatenated with TC number or SL
Test name in Atlantis reflects config type which consists of a several tests included in the config by the Etest team
Test name at tester may differ from test name in dashboard – follow methodology here
Make a uniform delimiter “-” (hyphen) within structure name except for additional details
Structure name, seat name, row instance are separated by “_” (underscore) – done post catalog gen.
Test name and structure name to be separated by pipe symbol “|” at CNAI dashboard level
Try to maintain equal number of delimiters across all structure types for ease of automation and text to column separation
Any additional detail must be added in appropriate position separated by a colon symbol “:” for ISO structures to separate chunks of data
Any additional detail must be added at the end of the structure name and before seat name with “_” (underscore) as delimiter
Delimiter

## Slide 4
No more test name aliasing between Etest and dashboard on x818 TC and on
Each config contains a list of tests depending on what config type it is
      PFT config consists of a larger subset than a config designed for an 2pt ISO structure
      Naming convention changes for ease of use, detailed drain/source pin information should be retained
      IDEFF was referred as IEFF -> IDEFF will be retained
      Current –voltage separator “/” (forward slash) was replaced with “_” (underscore) -> forward slash will be retained
      LOG of test name is added in some cases -> required test config update to calculate logarithm of current at Etest
      BTI tests drop current/voltage spec -> retain Etest output
Test Name ALIAS
BKM from x78D -> x78E -> 80C
Notes: Test Name BKM WW19.xlsx

## Slide 5
STRUCTURE_NAME_AS_TESTED to be the same as STRUCTURE_NAME in CNAI dashboard
Character limit is 64 reserved for structure name +TC information – 7 characters reserved for Etest; Etest can be restrictive, but alignment is needed
  Use PDK reference to align on naming convention
  Follow new metadata column entries in Atlantis intended for uniform and auto scalar generation – do not use structure name to generate device attributes, instead use device attributes to construct structure name
Structure Name
Atlantis Metadata column requirements (Ack: Andrew, Brian)
Limit to 64 chars
Device Ack: Wenjun, Brian, Andrew, Harap
Etest Ack: Habib, Farid
VT Flavor | Symbol
HVT | HVT
SVT | SVT
SRAM VT | SRAMVT
LVT | LVT
ULVT | ULVT
ULVTLL | ULVTLL
ELVT | ELVT
Ack: Habib, Etest
Notes: Move VT after diff width
Try with JMP and make a script

## Slide 6
Validator Tool 1: Atlantis-based Layout vs Schematic (LvS)
Validates for layout checks to check for routing fails, missing schematic, mismatch in layout and schematics, unintended connections etc.
Device attributes covered: PLY CD, #Gangs, #Legs, #Instances, Shared Legs
Inputs: LVS String
Output: Pass/Fail – Routing, Schematic, Mapping errors
Validator Tool 2: Excel macro-based structure name constructor and validator – owned by Device
Inputs: DUT class, Polarity, CH, LNR, #Legs, Cell Env, VT, etc
        Output: LVS string, STRUCTURE_NAME
Structure Name Validation
Device Ack: Harap
Ack: TCE team / Eduardo
Atlantis Metadata column requirements (Ack: Andrew, Brian)
Validator Tool 2 is a requirement pre-tape in for LVS string generation as well as post-tape-in/pre-Etest for verification of entered device attribute to Structure name mapping. Second validation is done after database is closed to prevent layout edits. More updates to follow in WW20’26 since this area is under active development.

## Slide 7
Library Offering
Segment | CH | Diff. Width | LNR | Z
Standard Logic | 110 | 27 | 13 | Z1
 |  | 31 | 17 | Z2
 |  | 35 | 21 | Z3
 |  | 40 | 26 | Z4
 | 132 | 31 | 17 | Z2
 |  | 35 | 21 | Z3
 |  | 40 | 26 | Z4
 |  | 46 | 32 | Z5
 |  | 49 | 35 | Z6
 | 165 | 31 | 17 | Z2
 |  | 40 | 26 | Z4
 |  | 52 | 38 | Z6
 |  | 62 | 48 | Z7
Turbo Logic | 110 | 72 | 58 | Z8
 |  | 72 | 26/58/26 | Z8
 | 132 | 86 | 35/72/35 | Z9
 |  | 72 | 58 | Z8
 | 165 | 86 | 72 | Z9
Segment | Library | CH | Diff. Width | LNR | Z
Column Logic | HCC | 114 | 27 | 13 | Z1
 |  |  | 31 | 17 | Z2
 |  |  | 37 | 23 | ?
 | HDC | 128 | 31 | 17 | Z2
 |  |  | 35 | 21 | Z3
 |  |  | 40 | 26 | Z4
 |  |  | 44 | 30 | ?
 | TPRF | 126 | 31 | 17 | Z2
 |  |  | 35 | 21 | Z3
 |  |  | 40 | 26 | Z4
 |  |  | 43 | 29 | ?
 | HDC2 | 132 | 31 | 17 | Z2
 |  |  | 35 | 21 | Z3
 |  |  | 40 | 26 | Z4
 |  |  | 46 | 32 | Z5
x81A
x81Z
Derived from Roberto’s table – WW17.4v, updated w/ 1281 PDK model WW20
Library Model Naming for 1281
BNPN PMOS
Diffmax
OPH
BNPN PMOS
x81A
OPH
BNPN PMOS
BNPN PMOS
Notes: Z convention vs Diff. Width – needs alignment

## Slide 8
Library Offering
Segment | Library | CH | Diff. Width | LNR | PFT
SRAM | HDC1 HDC5 | 192 | 26 | 12 | PU
 |  |  | 28 | 14 | PG
 |  |  | 30 | 16 | PD
 | HDC3 | 192 | 26 | 13 | PU
 |  |  | 28 | 14 | PG
 |  |  | 30 | 16 | PD
 | HDC4 HDC6 | 192 | 27 | 13 | PU
 |  |  | 28 | 14 | PG
 |  |  | 29 | 15 | PD
 | HDC2 | 198 | 27 | 13 | PU
 |  |  | 29 | 15 | PG
 |  |  | 32 | 18 | PD
 | HCC1 HCC2 | 228 | 27 | 13 | PU
 |  |  | 39 | 25 | PG
 |  |  | 47 | 33 | PD
Segment | Library | CH | Diff. Width | LNR | PFT
TPRF | TPRF1 | 315 | 49 | 35 | RP
 |  |  | 27 | 13 | PU
 |  |  | 46 | 32 | PG
 |  |  | 47 | 33 | PD
 | TPRF2 | 315 | 49 | 35 | RP
 |  |  | 27 | 13 | PU
 |  |  | 46 | 14 | PG
 |  |  | 47 | 16 | PD
x81Z
Derived from Roberto’s table – WW17.4v

## Slide 9
Structure Name - ROS
TESTNAME_CATEGORYCELLHEIGHT-DIFF-LEGS-VT-Style-FTI-ISO-LayoutHeight-(Routing)-Style-Additional_TCxx_Count
Inline Structure Example
X81ZROS132-Z5-2L-ULVT-NAN-STG11-FO3-SH-M1_TCxx_y
EOL Structure Example
X81ZROS132-Z5-2L-LVT-INV-STG11-FO3-SH-M2-WAC_TCxx_y
Ring Oscillator
Cell Height
Metal Gate
Single/Double Height Cell
N/P LNR
N/P Legs
#Stages
Test Chip
Row Instance
Metal Routing
Fan Out
Style/
Environment
ROS PFT and ROS follow style convention right after legs in place of environment for CMOS PFT consistency
Stages is replaced with Nesting, Fan out is replaced with Isolation in ROSPFT
Notes: PDK model names – 1278
CH, LNR, VT type –
1280
Diff box width
1281 reference – Andrew to share list of column names that will be present in Atlantis templates
Ask Wenjun to write this out based on PDK reference

## Slide 10
Structure Name - ROS PFT
TESTNAME_CATEGORYCELLHEIGHT-DIFF-LEGS-VT-Style-FTI-ISO-LayoutHeight-(Routing)-Additional_TCxx_Count
Inline Structure Example
ROSN132-Z3-2L-ELVT-NAN-1X1-IXI-SH-M1-WAC-6X_TCxx_y
EOL Structure Example
ROSP132-Z3-2L-SVT-AOI-10X10-IXI-SH-M2-STK-16X_TCxx_y
Polarity
ROS-env. PFT
Cell Height
Nesting
Metal Gate
Additional WAC/Instance Information
Single/Double Height Cell
LNR
Legs
Isolation
Style/
Environment
Test Chip
Row Instance
Metal Routing
Precedes with M – Matching Pair PFT , Structure instance to be added in additional section
Precedes with W – Within Die PFTs, Structure instance to be added in additional section
ROS PFT and ROS follow style convention right after legs in place of environment for CMOS PFT consistency
Notes: PDK model names – 1278
CH, LNR, VT type –
1280
Diff box width
1281 reference – Andrew to share list of column names that will be present in Atlantis templates
Ask Wenjun to write this out based on PDK reference

## Slide 11
Structure Name – LLE-neutral PFT
TESTNAME_CATEGORYCELLHEIGHT-DIFF-LEGS-VT-Environment-FTI-ISO-LayoutHeight-(Routing)-Additional_TCxx_Count
Inline Structure Example
NS132-Z5-1L-ULVT-CMOS-1X1-IXI-SH-M1-NOM_TCxx_y
EOL Structure Example
NS110-Z8-1L-ELVT-BCMOS-1X1-IXI-DH_TCxx_y
Polarity
LLE-neutral PFT
Cell Height
Nesting
Metal Gate
For PW skews, follow ISO convention in additional section
LNR
Legs
Isolation
Environment
Test Chip
Row Instance
Metal Routing
Precedes with M – Matching Pair PFT, Structure instance to be added in additional section
Precedes with W – Within Die PFTs, Structure instance to be added in additional section
FTI:PGD:CD:P5
PLY:PP:CD:45/12
PLY:OGD:CD:12
PLY:OGD:PP:45
BCMOS – Balanced NPN
LCMOS – LNR Max
OCMOS - OPH
Environment
Notes: BCMOS – Balanced NPN
LCMOS – LNR Max
OCMOS - OPH
Make comments
-CMOS_DH_LNRREF, *-CMOS_DH_LNRMAX80,

## Slide 12
Structure Name – Bitcell/Column/TPRF PFT
TESTNAME_CATEGORYCELLHEIGHT-DIFF-LEGS-VT-Environment-FTI-ISO-Bitcell-(Routing)-Additional_TCxx_Count
Inline Structure Example
SRN192-30-1L-PD-HCC1-SNXSN-SNXSN-M1_TCxx_y
EOL Structure Example
SRP192-30-1L-PU-HCC1-SNXSN-SNXSN-M1_TCxx_y
RFN315-49-1L-RP-TPRF1-SNXSN-SNXSN-M2_TCxx_y
SR192-HDC1BCLA_TCxx_y
Bitcell
Metal Routing
SRAM
Test Chip
Row Instance
Cell Height
Nesting
Metal Gate
Diff. Width
Legs
Isolation
DUT/
Environment
All SRAM PD/PG/PU are HVT
TPRF PD/PG/PU are HVT
TPRF1 RP is SVT; TPRF2 RP is ULVTLL
Ack: Divya, Andrew
phpsrhdc1pu
nhpsrhdc1pg
nhpsrhdc1pd
phpsrhdc2pu
nhpsrhdc2pg
nhpsrhdc2pd
phpsrhcc1pu
nhpsrhcc1pg
nhpsrhcc1pd
phprf1pu
nhprf1pg
nhprf1pd
nhprf1rp
phprf2pu
nhprf2pg
nhprf2pd
nhprf2rp
Notes: VT to be replaced from SRAM structure name – to PG/PD – VT type to be POR for bitcell PFT
What about target being attached to a given structure?
SRAM and logic co centering plots – needs documentation on which VT type is mapped
IREAD to look different – IR for stacked

## Slide 13
Structure Name - MLR
TESTNAME_CATEGORYCELLHEIGHT-DIFF-#ADF-VT-Environment-(Routing)-Additonal_TCxx_Count
Inline Structure Example
NM132-Z5-1ADF-LVT-CMOS-M1-NOM_TCxx_y
EOL Structure Example
PM110-Z8-2ADF-ELVT-UNI-NOM_TCxx_y
Polarity
Miller
Cell Height
Metal Gate
LNR
#Active Diffusion Tracks
Environment
Test Chip
Row Instance
Metal Routing
Notes: LNR max should be a number – character – what does PDK follow?

## Slide 14
FailmodeCH-PolarityDIFF-VT-(SDR)TSDRSkew_Additional_Detail_Magnitude_TCxx_y
Examples:
CTGOGD132-NZ5-ULVTLL-A:TCP:OGD:REG:N7_TCxx_y
TCNETE165-NZ6-LVT-SDR_TCxx_y
DIFFOGD110-PZ3-SVT-B:FTIML:OGD:CD:P2_TCxx_y
DIFFOGD110-PZ3-SVT-A:DPR:PGD:CD:N2_TCxx_y
Structure Name - ISO-FE
Fail Mode Segment
Cell Height
LNR
Test Chip
Row Instance
Polarity
Metal Gate
TSDR Layer
Direction
Skew Type
Magnitude
Type
Notes: My sub name is FailmodeTestRowName Now, I want to generate a full structure spread of every structure name in sheet 3, column 2 along with test row name in column 1 - there is one row of header in sheet 3 The structure name should be generated as follows: TSDRIdentifierCellHeight-PolarityDiffusionWidth-MetalGate-SkewIdentifier TSDRIdentifier is in column F Cellheight and Diff Width are in column J coupled together in the format 132Z4, Z4 is going to be Diffusion Width ​‌

## Slide 15
Structure Name – ADT
TESTNAME_CATEGORYCELLHEIGHT-DIFF-LEGS-VT-Environment-FTI-ISO-LayoutHeight-(Routing)-Additional_TCxx_Count
Inline Structure Example
PS165-Z6-1L-LVT-ADT-3X3-IXI-DH-M1-48X-STK_TCxx_y
EOL Structure Example
NS110-Z8-1L-LVT-ADT-3X3-IXI-DH-4X-STK_TCxx_y
Polarity
PFT
Cell Height
Nesting
Metal Gate
Single/Double Height Cell
LNR
Legs
Isolation
Two active diffusion type ADT
Test Chip
Row Instance
Metal Routing
Additional WAC/Instance Information

## Slide 16
Use old name to extrapolate what grouping is
Use new name to extrapolate what grouping is
Compare new and old names
Use LVS strings to make sure structure names are right
Spot check structures individually
Generate (Ask Agent)
Generate structure names that are compliant with this

## Slide 18
Structure Name – 82Z vs 80BR
TESTNAME_CATEGORYCELLHEIGHT-DIFF-LEGS-VT-Environment-FTI-ISO-LayoutHeight-(Routing)-Additional_TCxx_Count
80BR CMOS PFT
NS144-A50-1X1-IXI-L-CMOS_TC31_1
80BR CMOS PFT
ROSN-144-50-2L-INV-LVT_M1FECL_TC31_1
82Z CMOS PFT
NS-108-A36-1X1-IXI-LVT-CMOS_TCxx_y
82Z ROS PFT
NROSMOS-INV-L18-108H-FS_TC13_1
Cell Height
Metal Gate
N/P Diff.
#Legs
Metal Routing
Style/
Environment
Cell Height
Metal Gate
Environment
Nest/Roost
N/P LNR
N/P Diff.
Lego Type
Lego Type
Environment
Nest/Roost
Polarity
Polarity
Polarity
Polarity
Metal Routing
Metal Gate
Style/
Environment
N/P Diff.
Cell Height
CH | Diff. Width | LNR | Z
120 | 34 | 16 | Z2
 | 36 | 18 | Z3
 | 42 | 24 | Z4
108 | 30 | 12 | Z1
 | 36 | 18 | Z3
96 | 30 | 12 | Z1
92 | 30 | 12 | Z1
 | 34 | 16 | Z2
#Unique LNRs
12, 16, 18, 24

## Slide 19
82Z WIJT pull
82Z Addin Old Method
80BR Data from CNAI Addin

## Slide 20
Testchip | Etest Name | CNAI Name | Testname to Structurename Delimiter
X802Z | ROSN-108-32-2L-INV-LVT_M1BECL-WAC_TC31_1 | ROSPFT_NZ1_108H_2LG_LVT_BM1WAC_INV | _
X80C | ROSN-144-50-2L-INV-LVT-SH-M2_WAC_TC12_1 | ROSPFT_NZ3_144H_2LG_LVT_M2_INV | ¦
X82Z | NROSMOS-INV-L18-108H-FS_TC31_1 | ROSN108-Z3-L-1L-INV-1X1-IXI-SH-M1 | ¦
X81Z | ROSN132-Z3-E-2L-INV-1X1-IXI-SH-M1_TCxx_y | ROSN132-Z3-E-2L-INV-1X1-IXI-SH-M1-WAC-6X | ¦
^