## Slide 1
ISO E-test Scalar Catalog (1281 node)
496 structure variants covering 2180 buildsheet rows
Per variant: annotated unit-cell layout, counted leakage paths and the ScalarFormula
Generated by ScalarCalculation.py --pptx

## Slide 2
Executive summary -- ISO scalar calculator
Purpose
Fill the Scalar column (Scalar = 1 / fail-mode count) of the ISO E-test metadata buildsheet for every isolation structure and document the derivation (ScalarFormula)
so each value can be audited.
Input
ISO_Metadata_Input.csv -- the ISO buildsheet (one row per structure / test row). Columns used: StructureName, UnitCellSizeOgd/Pgd, ArraySizeOgd/Pgd, FTITracksUnit,
PolyPlugsUnit, TcnPlugsUnit, VcxPatternUnit (vg/vt vias), LO1/HI1ActiveTracks, DiffPatternUnit, CellHeight.
Method
1) Parse the buildsheet DSL (ranges a:b, strides a:b[N], rK end-relative tokens) into one Ogd x Pgd unit cell: FTI grid, gate and TCN segments (plug model), VG / VT
positions, LO1 / HI1 nets. 2) Apply the family rule (CTG, GATEGATE/EPIEPI/TCNTCN, DIFFOGD, DIFFCHN) to count fail modes per unit. 3) Multiply by ArraySizeOgd x
ArraySizePgd; Scalar = 1/N. 4) Group rows into geometry variants, render an annotated unit-cell snapshot per variant, build this deck.
Calibration
Plug model (plug V merges diffusion tracks V-1/V) and via-track -> diffusion-track mapping were verified against the 12 CTG132 chassis GDS layouts bundled in
ISO_LLM.bat; methodology per 'x1281z - ISO E-test Scalar calculations suggestion.pptx'.
Output
ISO_Metadata_Output.csv (input + Scalar + ScalarFormula) | ISO_Scalar_Review.csv (per-row derivation, intermediate counts, notes) | ISO_Scalar_Variants.csv (one line
per geometry variant) | snapshots/*.png (optional, named after the structure) | ISO_Scalar_Catalog.pptx (this deck).
Libraries
Python 3.12 standard library (csv, re, argparse, dataclasses, pathlib) for the calculation; matplotlib for the snapshots; python-pptx for the catalog. No other
dependencies.
Run
python ScalarCalculation.py --pptx ISO_Scalar_Catalog.pptx (add --keep-snapshots to retain PNGs; --snapshot NAME renders a single structure; --summary-pptx FILE
writes this summary without layout slides)
Scope / caveats
Via-chain rows (VT_MV / VG_MV / VCR_MV) are out of scope and left blank. Snapshots are schematic (track -> diffusion-cell mapping is approximate). Data
inconsistencies (e.g. LO1/HI1 tracks not matching the via tracks) are flagged in the Notes column rather than silently corrected.

## Slide 3
Coverage -- structure families and variant types
2581 buildsheet rows: 2180 scored across 496 geometry variants; 401 via-chain rows out of scope. Scalar spans 1/21600 .. 1/3.
Family | Rows | Variants | FailModes range | Leakage path counted | Variant types in the input
CTG | 461 | 132 | 5400 .. 21600 | OGD contact-to-gate leakage: active gate (VG) beside an active TCN (VT) across the spacer | A SDR reference (+PLYFSPCR/PLYFTCN CD skews); B/C/D gate vs TCN length combos; E VCR PGD skews; F VCRNUB OGD skews; G diff depop / block-EPI; H/I extra VG/VT in fail area; K/L density (DEN) variants
GATEGATE | 654 | 62 | 3300 .. 10800 | PGD gate tip-to-tip leakage (LO1 gate end facing HI1 gate end) | A 1TRK/2TRK gates; OC1/OC2/OC3 via removal (SDR count kept); 2TRK_4PP isolated sub-unit; C gate ETE through FTI (FTIML 1FC / FTISL HC) with OGD/PGD CD/REG skews
EPIEPI | 249 | 118 | 5760 .. 11520 | PGD epi (TCN-landed diffusion) tip-to-tip leakage | A 1TRK/2TRK reference; B epi-to-epi across FTI (OGD); C 4-TCN density; D VT closer to fail area; ESD/NES implant, PXL/NPXL/NDBI mask, GLK/LNK/PLG density variants
TCNTCN | 138 | 44 | 5760 .. 11520 | PGD TCN tip-to-tip leakage | A 1TRK/2TRK reference; B VCR/VCRNUB skews (+DEN); C 4-TCN density; D VT closer to fail area; TCP/TCN CD-REG skews; ESD/NES implant variants
DIFFOGD | 294 | 20 | 4200 .. 8400 | OGD diffusion-to-diffusion leakage across an FTI cut | A FTIML (1FC FTI cuts 2 device tracks) / FTISL (HC FTI cuts 1) with OGD/PGD CD/REG skews
DIFFCHN | 384 | 120 | 3 .. 2880 | Diffusion chain: transistors in series between LO1 and HI1 | A single gates (LEN3/6/12); B stacked gate pairs STKx1/STKx2; D serpentine 1FC/HC chains (~2xLEN gates); 60x multi-instance arrays; PXL/FTI skews

## Slide 4
Methodology
Scalar = 1 / FailModeCount
PGD end-to-end (GATEGATE, EPIEPI, TCNTCN)
FailModeCount = (# LO1<->HI1 tip-to-tip pairs per unit cell) x (# unit cells). A pair is a LO gate/TCN segment facing a HI segment end-to-end on the
same column (adjacent diffusion tracks, or across an FTI). GATEGATE rows with vias removed (OC1/OC2/OC3) keep the SDR count from the declared LO1/HI1
tracks.
OGD contact-to-gate (CTG)
FailModeCount = (# active PLY, i.e. gates with a VG) x (# diffusion tracks on which an active TCN -- a TCN with a VT -- runs beside the gate) x (#
unit cells). One fail mode per gate per track: leakage happens on either side of the gate, the two sides are not added. Every variant (incl.
VCR/VCRNUB types E/F) is counted from its own geometry.
OGD diffusion (DIFFOGD)
FailModeCount = (# active FTI columns) x (# device diffusion tracks each FTI cuts, LO diffusion on one side / HI on the other) x (# unit cells).
Diffusion chain (DIFFCHN)
FailModeCount = # active VG gates in series (transistors in the current path, stacked gates included); multiplied by the number of chains when chains
are stacked in an array (60x multi-instance rows).
Unit cells
ArraySizeOgd x ArraySizePgd from the buildsheet.
Source
All counts are derived from the buildsheet row (FTITracksUnit, PolyPlugsUnit, TcnPlugsUnit, VcxPatternUnit, LO1/HI1ActiveTracks, DiffPatternUnit,
array sizes). Via-track to diffusion-track mapping and the plug model were calibrated on the CTG132 chassis GDS bundled in ISO_LLM.bat.

## Slide 5
Scalar summary by structure family / type
FailModes = fail-mode count of the whole structure (Scalar = 1/FailModes); full per-variant detail in ISO_Scalar_Variants.csv and on the following slides
Family | Type | Variants | Rows | Cell heights | FailModes | Scalar | Design patterns (StructureName suffixes)
CTG | A | 24 | 165 | ch110 ch132 ch165 | 10800 | 9.25926e-05 | A:SDR:OGD:REF:2TRK; A:PLYFSPCR:OGD:CD:<SKEW>; A:PLYFSPCR:OGD:CD:0; A:PLYFTCN:OGD:CD:<SKEW>; A:PLYFTCN:OGD:CD:0
CTG | B | 6 | 6 | ch132 ch165 | 10800 | 9.25926e-05 | B:NGLK:OGD:REF:2TRK
CTG | C | 6 | 6 | ch132 ch165 | 10800 | 9.25926e-05 | C:NTLK:OGD:REF:2TRK
CTG | D | 6 | 6 | ch132 ch165 | 21600 | 4.62963e-05 | D:NLNK:OGD:REF:1TRK
CTG | E | 16 | 114 | ch110 ch132 ch165 | 21600 | 4.62963e-05 | E:VCR:PGD:CD:<SKEW>; E:VCR:PGD:CD:0; E:VCR:PGD:REG:<SKEW>; E:VCR:PGD:REG:0
CTG | F | 18 | 96 | ch110 ch132 ch165 | 21600 | 4.62963e-05 | F:VCRNUB:OGD:REG:<SKEW>; F:VCRNUB:OGD:REG:0; F:VCRNUB:OGD:CD:<SKEW>; F:VCRNUB:OGD:CD:0
CTG | G | 4 | 4 | ch165 | 10800 | 9.25926e-05 | G:DNU:OGD:REF:NDPI_2TRK; G:DNU:OGD:REF:BEPI_2TRK
CTG | G | 4 | 4 | ch165 | 21600 | 4.62963e-05 | G:DNU:OGD:REF:NDPI_4TRK; G:DNU:OGD:REF:BEPI_4TRK
CTG | H | 12 | 12 | ch132 ch165 | 10800 | 9.25926e-05 | H:SDR:OGD:DEN:1VG_PLY; H:SDR:OGD:DEN:2VG_PLY
CTG | I | 12 | 12 | ch132 ch165 | 10800 | 9.25926e-05 | I:SDR:OGD:DEN:1VT_TCN; I:SDR:OGD:DEN:2VT_TCN
CTG | K | 12 | 18 | ch110 ch132 ch165 | 5400 | 0.000185185 | K:SDR:OGD:DEN:NTLK; K:SDR:OGD:DEN:NGLK
CTG | L | 12 | 18 | ch110 ch132 ch165 | 10800 | 9.25926e-05 | L:SDR:OGD:DEN:NGLK; L:SDR:OGD:DEN:NTLK
GATEGATE | A | 24 | 180 | ch110 ch132 ch165 | 10800 | 9.25926e-05 | A:SDR:PGD:REF:1TRK_1PP; A:SDR:PGD:REF:2TRK_1PP; A:SDR:PGD:REF:OC1; A:SDR:PGD:REF:OC2
GATEGATE | C | 20 | 294 | ch110 ch132 | 3300 | 0.00030303 | C:FTIML:SDR; C:FTIML:OGD:CD:<SKEW>; C:FTIML:PGD:CD:<SKEW>; C:FTIML:OGD:REG:<SKEW>; C:FTIML:PGD:REG:<SKEW>; C:FTISL:SDR; C:FTISL:OGD:CD:<SKEW>; C:FT...
GATEGATE | SDR_PGD_REF | 6 | 54 | ch110 ch132 ch165 | 3600 | 0.000277778 | SDR_PGD_REF-2TRK_4PP
GATEGATE | SDR_PGD_REF | 12 | 126 | ch110 ch132 ch165 | 10800 | 9.25926e-05 | SDR_PGD_REF-OC3; SDR_PGD_REF-1TRK_1PP; SDR_PGD_REF-OC1
EPIEPI | A | 92 | 185 | ch132 ch165 | 5760 | 0.000173611 | A:SDR:PGD:REF:1TRK_1PP; A:SDR:PGD:REF:2TRK_1PP; A:GLK_OGD_DEN:1TRK_1PP; A:PLG_OGD_DEN:1TRK_1PP; A:LNK_OGD_DEN:1TRK_1PP; A:NPXL:PGD:REF:1TRK_1PP; A:...
EPIEPI | B | 12 | 30 | ch132 ch165 | 5760 | 0.000173611 | B:FTI:OGD:CD:<SKEW>; B:FTI:OGD:CD:NOM; B:NPXL_FTI:OGD:CD:<SKEW>; B:NPXL_FTI:OGD:CD:NOM; B:NDBI_FTI:OGD:CD:<SKEW>; B:NDBI_FTI:OGD:CD:NOM; B:NDBI_NPX...
EPIEPI | C | 12 | 32 | ch132 ch165 | 11520 | 8.68056e-05 | C:PXL:PGD:REG:<SKEW>; C:PXL:PGD:REG:NOM; C:SDR:PGD:DEN:NOM; C:PXL:PGD:CD:<SKEW>; C:PXL:PGD:CD:NOM; C:NPXL:PGD:REF:2TRK_1PP; C:NDBI_PXL:PGD:REG:<SKE...
EPIEPI | D | 2 | 2 | ch132 | 5760 | 0.000173611 | D:NPXL:PGD:DEN:2TRK_1PP; D:NDBI_NPXL:PGD:DEN:2TRK_1PP
TCNTCN | A | 29 | 96 | ch132 ch165 | 5760 | 0.000173611 | A:SDR:PGD:REF:1TRK_1PP; A:SDR:PGD:REF:2TRK_1PP; A:GLK_OGD_DEN:1TRK_1PP; A:PLG_OGD_DEN:1TRK_1PP; A:LNK_OGD_DEN:1TRK_1PP; A:TCP:PGD:CD:<SKEW>; A:TCP:...
TCNTCN | B | 6 | 24 | ch132 | 5760 | 0.000173611 | B:VCR:PGD:CD:<SKEW>; B:VCR:PGD:CD:NOM; B:VCR:PGD:REG:<SKEW>; B:VCR:PGD:REG:NOM; B:VCRNUB:PGD:CD:<SKEW>; B:VCRNUB:PGD:CD:NOM
TCNTCN | B | 1 | 1 | ch165 | 11520 | 8.68056e-05 | B:VCR:PGD:DEN:1TRK_1PP
TCNTCN | C | 7 | 16 | ch132 ch165 | 11520 | 8.68056e-05 | C:SDR:PGD:DEN:2TRK_1PP; C:TCP:PGD:CD:<SKEW>; C:TCP:PGD:CD:NOM; C:DENTCP:PGD:CD:<SKEW>; C:DENTCP:PGD:CD:NOM; C:DENTCP:OGD:CD:<SKEW>; C:DENTCP:OGD:CD...
TCNTCN | D | 1 | 1 | ch132 | 5760 | 0.000173611 | D:SDR:PGD:DEN:2TRK_1PP
DIFFOGD | A | 10 | 98 | ch110 ch132 | 4200 | 0.000238095 | A:FTISL:SDR; A:FTISL:OGD:CD:<SKEW>; A:FTISL:PGD:CD:<SKEW>; A:FTISL:OGD:REG:<SKEW>; A:FTISL:PGD:REG:<SKEW>
DIFFOGD | A | 10 | 196 | ch110 ch132 | 8400 | 0.000119048 | A:FTIML:SDR; A:FTIML:OGD:CD:<SKEW>; A:FTIML:PGD:CD:<SKEW>; A:FTIML:OGD:REG:<SKEW>; A:FTIML:PGD:REG:<SKEW>
DIFFCHN | A | 4 | 6 | ch110 ch132 ch165 | 3 | 0.333333 | A-LEN<n>-SDR:Z:REF:NOM
DIFFCHN | A | 10 | 32 | ch110 ch132 ch165 | 6 | 0.166667 | A-LEN<n>-SDR:Z:REF:NOM; A-LEN<n>-PXL:PGD:CD:<SKEW>; A-LEN<n>-PXL:PGD:CD:NOM
DIFFCHN | A | 4 | 18 | ch110 ch132 ch165 | 12 | 0.0833333 | A-LEN<n>-SDR:Z:REF:NOM
DIFFCHN | B | 16 | 36 | ch110 ch132 ch165 | 16 | 0.0625 | B-STKx1FLEN<n>-SDR:Z:REF:NOM; B-STKx2FLEN<n>-SDR:Z:REF:NOM
DIFFCHN | B | 8 | 12 | ch110 ch132 ch165 | 32 | 0.03125 | B-STKx1FLEN<n>-SDR:Z:REF:NOM; B-STKx2FLEN<n>-SDR:Z:REF:NOM
DIFFCHN | B | 8 | 12 | ch110 ch132 ch165 | 48 | 0.0208333 | B-STKx1FLEN<n>-SDR:Z:REF:NOM; B-STKx2FLEN<n>-SDR:Z:REF:NOM
DIFFCHN | B | 2 | 2 | ch110 | 2880 | 0.000347222 | B-60xSTKx2FLEN<n>-SDR:Z:REF:NOM
DIFFCHN | D | 4 | 18 | ch110 ch132 ch165 | 11 | 0.0909091 | D-1FCLEN<n>-SDR:Z:DEN:NOM
DIFFCHN | D | 20 | 82 | ch110 ch132 ch165 | 19 | 0.0526316 | D-1FCLEN<n>-SDR:Z:DEN:NOM; D-HCLEN<n>-SDR:Z:DEN:NOM; D-1FCLEN<n>-FTI:PGD:REG:<SKEW>; D-1FCLEN<n>-FTI:PGD:REG:NOM; D-1FCLEN<n>-FTI:OGD:REG:<SKEW>; D...
DIFFCHN | D | 4 | 6 | ch110 ch132 ch165 | 31 | 0.0322581 | D-1FCLEN<n>-SDR:Z:DEN:NOM
DIFFCHN | D | 4 | 6 | ch110 ch132 ch165 | 48 | 0.0208333 | D-1FCLEN<n>-SDR:Z:DEN:NOM
DIFFCHN | D | 4 | 6 | ch110 ch132 ch165 | 1140 | 0.000877193 | D-60x1FCLEN<n>-SDR:Z:DEN:NOM
DIFFCHN | LEN10FC | 12 | 54 | ch132 ch165 | 19 | 0.0526316 | LEN<n>FC-D:PXL:PGD:REG:<SKEW>; LEN<n>FC-D:PXL:PGD:REG:NOM; LEN<n>FC-D:PXL:PGD:CD:<SKEW>; LEN<n>FC-D:PXL:PGD:CD:NOM
DIFFCHN | LEN6 | 20 | 94 | ch132 ch165 | 6 | 0.166667 | LEN<n>-A:PXL:PGD:REG:<SKEW>; LEN<n>-A:PXL:PGD:REG:NOM; LEN<n>-A:PXL:PGD:CD:<SKEW>; LEN<n>-A:PXL:PGD:CD:NOM; LEN<n>-A:FTI:OGD:REG:<SKEW>; LEN<n>-A:F...